Model: Fingerprint Lock CJ-6686

Installation Instruction:

Mortise Choice

If needing 60mm latch,Please fix the screw to the picture

If needing 70mm latch,Please fix the screw to the picture

Hole Sketch

Installation Drawing Dimension Technical Specifiation: Item# Description Technical Parameters 1 Sensor Bright background,for totally resolving the issue of remaining fingerprints 2 Resolution factor 560 dpi 3 Sensor resistance to destruction 4H pencil 20cm constant impact for 1000 times resulting in no destruction 4 Startup time ＜1s 5 Contrast 1:N 6 FRR Less than or equal to 1%(≤1%) 7 FAR Less than or equal to 0.0001%(≤0.0001%) 8 Angle of finger application ±60° 9 Fingerprint registration module One time of registration producing one module 10 Fingerprint update Fully automatic update technology 11 ingerprint template storage Automatic storage of fingerprint template when batteries are changed 12 Max figerprint capacity 150 fingerprints 13 Light interference Protection against direct sunshine 14 Collector Hard glass,nano-treated surface,extremely resistant to friction 15 Static power consumption Less than 30uA 16 Dynamic power consumption Working current between 150-300mA 17 Working voltage Intemational standard batteries,4*1.5V alkaline batteries,DC6V 18 Service life of batteries For opening a door 15,000 times in nomal cases 19 Power supply Batteries,plus extemal power supply 20 Password capacity 78 21 Spare voltage for working voltage 9V 22 Waming voltage 4.8V 23 Electrostatic resistance ＞15000V 24 Working temperature for fingerprint -20℃～60℃ 25 Working temperature for keypad -30℃～70℃ 26 Working humidity 10%-97% 27 Storage temperature -30℃～70℃ 28 Password setting Random combination 29 password length 8 digits 30 Spare power supply for working voltage 9V 31 Area of collection 18.2mm(L)X16mm(W)